## Slide 1: WiFi
Version 3

## Slide 2: Overview
Protocols
WiFi & OSI Layers
Antenas
Propagation
Access Methods
Security concerns
Security techniques
  WEP
  WPA/WPA2

## Slide 3: 802.11
Standard | Freq Range | Bandwidth | Geo-Range
802.11b | 2.4GHz | 11Mbps | 100 m
802.11a | 5 GHz | 54 Mbps | 50 m
802.11g | 2.4 GHz | 54 Mbps | 100 M
802.11n | 2.4 or 5.0 GHz | 600 Mbps | Indoor: 70 m Outdoor: 250 m
802.11ac (Wave 1) | 5 GHz - 3 data streams | 1.3 Gbps | Indoor: 70 m Outdoor: 250 m
802.11ac (Wave 2) | 5 GHz - 4 data streams | 3.47 Gbps | Indoor: 70 m Outdoor: 250 m
802.11ac (Wave 3) | 5 GHz - 8 data streams | 6.93 Gbps | Indoor: 70 m Outdoor: 250 m
Ref: West, Andrews, Dean. Network + Guide to Networks, p. 323

## Slide 4: WiFi and OSI Layers
WiFi Similar to Wired
WiFi different

## Slide 5: WiFi - Layer 1 - The Physical layer
At this layer the transceiver is controlled to access the medium
Unlike a bounded, wired medium, WLANs operate "over the air" and are subject to an entirely different set of rules for accessing and controlling the medium

## Slide 6: WiFi - Layer 1 - The Physical layer
Wired networks can detect and mitigate data collisions
wireless networks cannot detect collisions
protocols allow access and control of the medium and to avoid collisions

## Slide 7: WiFi - Layer 1 - The Physical layer
Wireless networks experience external interference and disruptions

## Slide 8: WiFi - Layer 1 - The Physical layer
Wireless networks do not require physical access (to some degree)
Only need to be within range of an access point
Wireless presents significant operational and security challenges at Layer 1

## Slide 9: WiFi - Layer 1 - The Physical layer
Frequency Band (2.4 or 5GHz)
Bandwidth 20/40/60/80/160Mhz)
Modulation Types: DSSS, FHSS, OFDM, BPSK, QAM, QPSK, etc

## Slide 10: WiFi – Layer 2 - DataLink
Two sublayers: the Logical Link Control (LLC) sublayer and the Medium Access Control (MAC) sublayer
  The LLC receives an IP packet from the Network layer above it and encapsulates the data with addressing and control information
  This packet, now called a frame, is passed to the MAC, which modifies the addressing and control information in the frame header to ensure the data is in the proper form for application to the Physical layer
The MAC then passes the frame to the PHY, which modulates the data according to the PHY standard in use (DSSS, OFDM), and transmits the bits as RF
The process is reversed at the receiving end.
WiFi includes things on the data layer that are considered to be on different layers on the OSI stack (such as encryption), but are not considered at all on the TCP/IP stack

## Slide 11: Antennas
Unidirectional – also called a directional antenna
  Point-to-Point Link
Omni-directional – Sends (and receives) signals at same strength in all directions.
  Highly mobile
  Send/receive to/from many

## Slide 12: Propagation
The way in which a signal travels
LOS – Straight line TX to RX
Degradations
  Fading – Obstacles or barriers
  Attenuation - Distance
  Interference – From electromagnetic waves (EMI)
  Refraction (into/through a different transmission medium that changes the wavelength, speed, or other characteristic (e.g., Water)
  Reflection (obstacle or bounce back)

## Slide 13: WiFi - Access Methods
CSMA/CA
  Carrier Sense, Multiple Access/Collision Avoidance
  Minimizes occurrence but can’t detect if collision occurs
Ref: West, Andrews, Dean. Network + Guide to Networks, p. 326

## Slide 14: CSMA/CD Access Method
Check for Transmissions
Activity
Brief Pause
Send Msg
TX Complete
Yes
No
Collision?
Brief Pause
No
Yes
For Review: Wired Network
Notes: Step 1: If no TX in progress, wait
if traffic, wait a brief period, and then check again
Step 2: Dest Receives, verifies accuracy, and then send ACK
If no ACK, then try resend

## Slide 15: Hidden Node
Why WiFi uses a different Access Method

## Slide 16: CSMA/CA Access Method
Check for Transmissions
Activity
Brief Pause
Send Msg
TX Complete
Adapted from: West, Andrews, Dean. Network + Guide to Networks, p. 327
Yes
No
Send RTS
Cleared
To
Send?
No
Yes

## Slide 17: Hidden Node Problem
Access
Point
Client
Client
Distance too great to see each others transmission
RTS/CTS used to solve this problem
This is why Request to Send is needed

## Slide 18: Hidden Node Problem
https://upload.wikimedia.org/wikipedia/commons/2/2b/Wifi_hidden_station_problem.svg
Different View
B = AP Range
C = TX Range
A = TX Range
This is why Request to Send is needed

## Slide 19: Solve Hidden Node  RTS/CTS
A.k.a. CSMA/CA

## Slide 20: Channels
Channels help with traffic congestion and interference

## Slide 21: 2.4 GHz Channels

## Slide 22: Channels 2.4 GHz
Lots of channels, but only 3 distinct separations
1, 6, 11,

## Slide 23: 5 Ghz Channels
Channel Planning Best Practices for Better Wi-Fi - Ekahau
Available channels on the 5 GHz Wireless network – Keenetic
Wi-Fi Channels, Frequency Bands & Bandwidth » Electronics Notes (electronics-notes.com)

## Slide 24: Heat Maps

## Slide 25: Heat Maps

## Slide 26: Security

## Slide 27
While at the coffee shop, your PC is constantly scanning for and talking to access points.
(Think Evil Twin)
SRC: https://commons.wikimedia.org/wiki/File:Andrew_Bogott%27s_occasional_workspace.jpg

## Slide 28: Security Requirements
Security between two network entities should provide the following
  Authentication
  Integrity
  Privacy
    Primarily eavesdropping attempts

## Slide 29: WiFi Threats
Man-in-the-middle attacks
  (Most Common)
Rogue access points
Denial of service
Other threats include:
  Ad hoc networks
  MAC Spoofing
  Network Injection

## Slide 30: Additional WiFi Threats
War Driving
War Chalking (symbols)
WPA Attacks (cracking keys)
WPS Attacks (Auto setup)
Evil Twins
https://www.safervpn.com/blog/10-public-wi-fi-security-threats/
Notes: Evil Twin – same as rogue access point and leads to man in the middle attacks

## Slide 31: Man-In-The-Middle Attacks
Attacker intercepts messages in a public key exchange and retransmits them.
Attacker substitutes his own public key for the requested one.
Original parties believe they are just communicating with each other
The attacker has access to both user’s messages
Notes: -Form of eavesdropping

## Slide 32: Typical Man-In-The-Middle Attack
Bob
Bad
Guy
Alice
Bob’s Key
Bob’s Key
Bad guy gets in the middle
Keeps keys and replaces with his own key
Alice sends Key
Bad guy keeps Alice’s key
Send own key to Bob
Bob send account #
Bad guy sends
His account #
Alice sends $$$ to
Bad guy’s account

## Slide 33
WiFi

## Slide 34: Man-In-The-Middle Attacks (cont.)
Bob
Access
Point
Pineapple Joins the
Access point
Pineapple sends all traffic back from AP
But gets to look at all traffic

## Slide 35: Pineapple

## Slide 36: Denial of Service
An attempt to make a machine or network unavailable
Many different methods of attacks
  Internet Control Message Protocol Flood
  SYN flood
  Teardrop attacks
Notes: -Attacks usually overload the server
-Causes the victim to no longer communicate adequately

## Slide 37: DoS: ICMP Flood (SMURF Attack)
Distributed DoS attack in which large numbers of ICMP packets with the intended victim's spoofed source IP are broadcast to a computer network using an IP Broadcast address.
Devices on the network respond to the ICMP with a reply to the source IP address.
Think back to how CSMA/CA works, and note how sensitive WiFi is to DoS

## Slide 38: Rogue Access Points
A wireless access point on a company network without authorization
Often used to conduct a man-in-the-middle attack
To combat rogue WLANs
  Use a wireless scanner
  Wireless intrusion detection/prevention system (IDS/IPS)
  Harden/Secure the network

## Slide 39: WiFi Security
WEP, WPA, WPA Enterprise

## Slide 40: Wireless Network Security Methods
WEP – Wired Equivalent Privacy
WPA- Wi-Fi Protected Access
WPA2/802.11i

## Slide 41: Wired Equivalent Privacy (WEP)
Original encryption protocol
  IEEE 802.11 wireless LANs
Same level of security as wired networks
No longer recommended
Easily cracked in seconds by sniffing encrypted traffic
Notes: -Easily Hacked

## Slide 42: Wi-Fi Protected Access (WPA)
Replaces WEP
Stronger encryption (but still weak)
Standard Encryption technology
  TKIP – Temporal Key Integrity Protocol

## Slide 43: Wi-Fi Protected Access 2 (WPA2)
Replaced WPA on all Wi-Fi hardware since 2006
Government grade security by combining the AES encryption algorithm and 802.1x-based authentication
Two versions
  Enterprise – Server authentication 802.1x
  Personal – AES pre-shared key
Backward compatible with WPA
Uses CCMP

## Slide 44: WPA2 Personal vs WPA2
Personal
  Uses pre-shared key to optimize its effectiveness without an authentication server
    Used in small office and home environments
Enterprise
  Caters to big businesses
  Uses open system authentication in its first phase and the Extensible Authentication protocol method and 802.1x protocol in its second phase

## Slide 45: WPA2 Authentication
IEEE 802.1x
WPA2 personal doesn’t require an authentication server
WPA2 enterprise consists of the following:
  Client
  Access Point
  Authentication Server

## Slide 46: Why use WPA2?
WPA2 defends against
  Man-in-the-middle attacks
  Weak Keys
  Packet forging
  Brute-force attacks

## Slide 47: WPA2 flaws
Can’t withstand a physical layer attack such as:
  Data flooding
  Access point failure
Vulnerable to a DoS attack

## Slide 48: WPA 3?
January 2018 -- Wi-Fi Alliance announces WPA3 as a replacement to WPA2
Uses 192-bit encryption and individualized encryption for each user
The Wi-Fi Alliance also claims that WPA3 will mitigate security issues posed by weak passwords and simplify the process of setting up devices with no display interface
https://en.wikipedia.org/wiki/Wi-Fi_Protected_Access

## Slide 49: Summary
Protocols
WiFi & OSI Layers
Antenas
Propagation
Access Methods
Security concerns
Security techniques
  WEP
  WPA/WPA2

## Slide 50
?